## Slide 2: Flight Controller for Autonomous Drones
Student: Supervisor(s):
Marcus Christiansen Søren Hansen
Nils Axel Andersen

## Slide 3: Outline
Simulation
  Derive equations required for simulation
Controller Design
  Design criterias and performance of the simulated controllers
Implementation
  Implementation of controllers and tracking system, and their performance on a real system
Conclusion
Disussion about the overall project, the results and about future works
Notes: Discussion will come for each section

## Slide 4: Objectives
Simulate a Hexacopter in Simulink.
Use the simulation to design a positional controller for X, Y, Z, and Yaw.
Implement controllers on a real-time system.
  Z-domain implementation
Implement a global positioning System.
  GNSS (Simulated with OptiTrack)
Implement an accurate positioning system for precision tasks.
  Aruco Tracking
Notes: Limitations The limitations of the project can be summarized into the following points: 1. All testing has to be done indoors due to Danish drone regulations and safety. 2. The project builds on top of an existing project, which limits the project. For instance in regards to hardware. The software has to be able to run on a Raspberry Pi. 3. The time frame of the project is approximately 5 months

## Slide 5: Mission
Fly to the house. The house is located 1 km from the takeoff location. When the drone is near the house, locate the landing pad which is 20 × 20 cm. The landing pad is located in the back garden and is close to a tree, which allows for an 8 cm margin of error in position. Place the parcel on the pad and return to base. When approaching a house, the drone should limit its speed to 1 m/s due to safety concerns of the occupants of the house.
The low speed would ensure that if something happened and the drone was approaching a person, that person would be able to get out of the way.

## Slide 6: Simulation

## Slide 7: Simulation - Motor
Type:
  MultiStar 700KV
  BLDC
  14.8 volt rating
  0.134 Ohm
Goal:
  Get relation between PWM and angular velocity
Notes: KV 700 = 10360 RPM
Batt 14.8 volt (4s)
0.083 ohm in matlab (Probably wrong)

## Slide 8: Simulation - Motor
Electrical System
Mechanical System
Combined
Notes: Kirchofs law. Sum of all voltage in a closed loop is 0.
T_drag is the props giving resistance
Inductance is ignored
In analyzing the motor, we can usually ignore the inductance since the L/R electrical time constant is much shorter than the mechanical time constant determined by the rotor's moment of inertia

## Slide 9: Simulation – Forces
Linear
  Propeller force
  Gravity
  Air viscosity
Rotational
  Motor torque
  Thrust vector offset from center of mass
Notes: Air viscosity. Only important for position control
Has 6 DOF, but can only apply a force in its own relative z direction

## Slide 10: Simulation – Forces
Linear Dynamics
Notes: Kd - Air viscosity. Only important for position control
K is constant describing relation between angular velocity and the lift generated

## Slide 11: Simulation – Forces
Rotational Dynamics
Notes: L_x and L_y describes point of lift.
B is drag coefficient for propellers
I_xx I_yy should be the same. I_zz is not
Drone can be decribed as a disc when talking inertia.
Final equation is angular acceleration around x y and z.
Last equation gives angular acceleration for x y and z.

## Slide 12: Simulation - Model

## Slide 13: Simulation - Model

## Slide 14: Controller Design

## Slide 15: Controller Design - Type
PI-Lead
  Simple design
  Single Input Single Output
Linear Quadratic Regulator
  Optimization approach
  Difficult to tune afterwards
  Multiple Input Multiple Output
Model Predictive Control
  Comparable to LQR
  Optimization approach
  Generally considered more complex
Notes: Requirements - Keep it simple
PID already used

## Slide 16: Controller Design - Criterias
High Phase and Gain Margin
  Stability against imperfect dynamics
Realistic Constant Gain
  Avoid saturating actuator input
Avoid I Term
  Windup problem
Avoid Fast Rise Time
  Less agressive drone
Discretization
  Billinear transform for controllers
  Zero Order Hold for system
Notes: High Phase and Gain Margin
Wrong value for ohm
Avoid I Term
Windup problem especially with height control
Avoid Fast Rise Time
Safer as well

## Slide 17: Controller Design - Linearization
Notes: Slight mistake – Pitch/Roll out should be velocity. Same for yaw.

## Slide 18: Controller Design – Pitch/Roll TF
Notes: Gposcl output is radians
Step by step:
Apply pitch velocity controller to found TF and close loop
Integrate to get pitch position
Apply pitch position controller and close loop
Multiply with force required for hover. This gives the force applied based on the drones tilt
Integrate to get drone velocity

## Slide 19: Controller Design
Notes: Lead term i measurement. Fungere som filter på measurement samt er mere robust over for disturbance, på bekostning af rise time.
Største fordel er mindre overshoot.

## Slide 20: Controller Design
Notes: Lead term i measurement. Fungere som filter på measurement samt er mere robust over for disturbance, på bekostning af rise time.
Største fordel er mindre overshoot.

## Slide 21: Controller Design – Height Control
PI-Lead design
  Simple
  Requires I term
Cascading P P-Lead design
  Allows for velocity control
  More complex

## Slide 22: Controller Design – PI-Lead Height
Notes: Actuator value is based on the error term and can therefore be very large if a large change in height is required.
Agressive lead factor of 0.07
Gain margin: 20 dB
Phase margin: 45 degrees

## Slide 23: Controller Design – Cascading Height
Notes: Actuator input saturation is not an issue because pos controller max output is 1 to -1
Agressive lead factor of 0.07
Gain margin: 22 dB
Phase margin: 66 degrees

## Slide 24: Controller Design – Height Simulation Evaluation
Cascading
  Rise time: 8.1 seconds
  Settle time: 16.5 seconds
  Max velocity: 0.55 m/s
  Max overshoot: 0.5 meter
PI-Lead
  Rise time: 6.1 seconds
  Settle time: 13.5 seconds
  Max velocity: 1.05 m/s
  Max overshoot: 0.13 meter
Test parameters
  Reference height: 4 Meters
  Prefered max velocity: 0.5 m/s
Notes: Simulated controllers

## Slide 25: Controller Design – X/Y Control
Notes: Cascading design
Less aggressive lead factor of 0.3

## Slide 26: Controller Design – X/Y Control
Test parameters
  Reference position: 4 meters along x-axis
  Prefered max velocity: 1 m/s
Results
  Rise time: 5.2 seconds
  Settle time: 3 seconds
  Max velocity: 1 m/s
  Max overshoot: 3 cm
  Steady state error: 3 cm

## Slide 27: Implementation

## Slide 28: Implementation – Aruco Tracking
Aruco Tracking
  Gives position and orientation of marker relative to drone.
Objectives
  Get Intrinsic Camera Matrix
    Allows for projecting a point in image plane to a line in 3d space
  Align Drone Frame with Camera Frame
  Aruco Transform
Notes: Note that FOV is decreased

## Slide 29: Implementation – Align Camera with Drone
Notes: Point where camera is attached.
Take note that it aligns wit y=0 but not x=0.

## Slide 30: Implementation – Aruco Transform
Notes: Misleading variable names
Orientation aligns with world. Position is relative to drone

## Slide 31: Implementation – Aruco Performance
Notes: Blue is optitrack (Ground truth)
Loss of tracking
Camera not placed perfectly in the center of the drone
Low FOV
Low Resolution

## Slide 32: Implementation – Aruco Performance
Notes: Clearly shows the alignment issue

## Slide 34: Implementation – Controller Performance
Position Controller Results
  Rise time: 11~ seconds
  Settle time: 3~ seconds
  Max velocity: 0.68~ m/s
  Max overshoot: 4~ cm
  Steady state error: 5~ cm
Imperfect test case
Notes: Stage 1 is where the drone has found an Aruco code and navigates toward it.
Stage 2 is where the drone is at the Aruco code.
Stage 3 is where the drone loses tracking and starts drifting until the Tracking Abort System kicks in (See Section 4.4) and the drone starts to hold its position.
Stage 4 is where the pilot takes manual control of the drone and lands it.

## Slide 35: Implementation – Controller Performance
Cascading
  Rise time: 8 seconds
  Settle time: 3 seconds
  Max velocity: 1 m/s
  Steady state error: 0.6 meters
  Oscillates
PI-Lead
  Rise time: Misleading
  Settle time: Unstable
  Max velocity: 0.5 m/s
  Steady state error: 1.3 meters

## Slide 36: Implementation – Controller Performance
Issues encountered with height controller
Notes: Left graph shows what happens if the position controller is allowed to go above 1 m/s
Why the PI-Lead didnt work
Couldnt disable height controller.

## Slide 37: Conclusion

## Slide 38: Conclusion
Simulate a Hexacopter in Simulink.
Use the simulation to design a positional controller for X, Y, Z, and Yaw.
Implement controllers on a real-time system.
Implement a global positioning System.
Implement an accurate positioning system for precision tasks.
Notes: 4: Simulated by using OptiTrack

## Slide 39: Future Works
Aruco Tracking
  Better processor
  Camera gimbal or 180 degree camera
Gyro Drift
  Re-callibrate Madgwick filter
Safety Measures
  Loss of motor recovery system
  Human detection
  Auto landing
  Rigid frame
Test controllers again
  PI-Lead height controller
  Position controller
Notes: Gyro drift: Linear acceleration seems to be acting too slow
Test controllers again: PI-Lead was never tested after fix. Position controller should be tested against

## Slide 40: Questions?